| Specification / Document Review Schedule |
| --- |
| Contract Name: XXXX City Council Ref xxxxxx | Responsibility * NZRF - Contractor AI - Cont Inspector ENG - Engineer | Control Documents ** WI - Work Instruction JC - Job Card IR - Inspection Report | Inspection Action *** I - Inspect M - Measure N - Notify/Report |
| Prepared By: NZRF | Date: |  |  |  |
| Approved By: | Date: |  |  |  |
| Task | Spec. / Document | Task Response * | Requirement or Compliance Criteria | Document Control ** | Inspection Response * | Requirement Action *** | Record Required | Notes | Action Completed (Sign/date) |
| Site Safety Plan | Cx.x & Cx.x of Contract | NZRF | Refer C1.4 | Safety Plan | ENG | I | Safety Plan | Safety Plan to include TMPs |  |
| Traffic Management _ Level 1 | Cx.x.x of Contract | NZRF | Level 1 TNZ CoPTTM | TMP | NZRF/ ENG | I | TMP |  |  |
| Traffic Management _ Level 2 | Cx.x.x of Contract | NZRF | Level 2 TNZ CoPTTM | TMP | NZRF/ ENG | I | TMP | Significant quantities of Level 2 off-peak |  |
| Environmental Management Plan | Cx.xx & Cx.x.x of Contract | NZRF | Manage hydrocarbons, protect vegetation and waterways, effective silencers | CQP | ENG | I | CQP |  |  |
| Programme of Works | Cx.x of Contract |  |  |  |  |  |  | Four Wards |  |
| Plant Certification | P/22:2006 / T/8:2006 | NZRF | Certs current at all time, six monthly verification | NZRF Checklist | T/8 testing officer | I | T/8 Certs & Register | Certs held with applicator |  |
| Paint Type & Approval | Clause Cx xx.x of Contract / M/7 | NZRF | Chlorinated Rubber Based Roadmarking Paint M/7 Notes P/12:2000 (Brands as follows) | CQP | ENG | I | Batch Certs & DJR |  |  |
| White Paint (Roadmarking & Carparks) | Clause Cx x.x of Contract / M/7 | NZRF | Brand? | CQP | AI |  | Batch Certs & DJR |  |  |
| Yellow Paint (Roadmarking & Hydrants) | Clause Cx xx.x of Contract / M/7 | NZRF | Brand? | CQP | AI |  | Batch Certs & DJR |  |  |
| Glass Bead Type & Approval | TNZ P/22: 2006 / AS/NZS 2009:2006 | NZRF | Type B Quality requirements for particle size and optical quality | CQP | AI | I | Compliance Certs issued by NATA/IANZ lab | Sample required on request |  |
| Blue Paint (SV & PV Valves) | Clause Cx xx.x of Contract | NZRF | Zenith Blue ID 880-710 from Protective Paints Ltd? | CQP | AI |  | Batch Certs & DJR | Approval required for alternative supplier |  |
| Red Paint (Zone Valves) | Clause Cx xx.x of Contract | NZRF | Bright Roadmarking Red ID 880-21V from Protective Paints? | CQP | AI |  | Batch Certs & DJR | Approval required for alternative supplier |  |
| Raised Pavement Markers – Reflectorised – Surface Fixing | Clause Cx xx.x of Contract / M/12 | NZRF |  | CQP | AI |  |  | Sample required on request |  |
| Raised Pavement Markers – Reflectorised – Anchor Dowell Fixing | Clause Cx xx.x of Contract / M/12 | NZRF |  | CQP | AI |  |  | Sample required on request |  |
| Raised Pavement Markers – Audio Dome Dowelled | Clause Cx xx.x of Contract / M/12 | NZRF |  | CQP | AI |  |  | Sample required on request |  |
| Raised Pavement Markers – Ceramic Marker | Clause Cx xx.x of Contract / M/12 | NZRF |  | CQP | AI |  |  | Sample required on request |  |
| Hrs of Work | Cx.x of Contract | NZRF | 7:00am to 7:00pm, 9:00am to 3:00pm on main roads & arterials | CQP |  |  |  |  |  |
| Site Prep / Sweeping | Cx x.x of Contract | NZRF | Sweeping of chip is NZRF responsibility |  | NZRF | I |  |  |  |
| Paint Build-up | Cx.x of Contract | NZRF |  |  |  | N | Monthly Report | Inspection required to eliminate un-necessary film paint build-up |  |
| Marking layouts | MOTSAM Part II | NZRF |  | WI | NZRF | I |  |  |  |
| Marking locations (thermo/paint) | Contract/ P/22:2006 | NZRF |  | WI | NZRF | I |  |  |  |
| Width | Contract/ P/22:2006 | NZRF | -5% +10% | WI | NZRF | M |  |  |  |
| Paint thickness - repaint | Cx.x of Contract / P/22:2006 | NZRF | 150um min | WI | NZRF | M |  |  |  |
| Paint thickness - new work | Cx.x of Contract / P/22:2006 | NZRF | 200um min | WI | NZRF | M |  |  |  |
| Target paint usage rate - repaint | 13.1 (c) of P/22:2006 | NZRF | Min of 27.8L/km for 100mm | WI | NZRF | M | DJR | Paint Computer |  |
| Target paint usage rate – new work | 13.1 (c) of P/22:2006 | NZRF | Min of 37.0L/km for 100mm | WI | NZRF | M | DJR | Paint Computer |  |
| Bead application rate – all roads | 13.3.1 of P/22:2006 | NZRF | Min 275g/m2 | WI | NZRF | M | DJR | Usage Record |  |
| RPM Inspections | P/14:1995 | NZRF | Cause ?? | IR | ENG | N |  |  |  |
| RPM location | P/14:1995 | NZRF |  | WI |  |  |  |  |  |
| Materials Records | Clause Cx xx.x of Contract / 16.0 of P/22:2006 | NZRF | P/22 – Clause 16 amended by Cx xx | WI | NZRF |  | IR |  |  |
| Inventory location | Clause Cx xx.x of Contract | NZRF |  |  |  |  | XX C C RAMM Data System |  |  |